CSULB LASER SAFETY TRAINING QUIZ

- The three characteristic properties of laser light are monochromatic, directional, coherent.   T or F

- The first rule of laser safety is never under any circumstances look into any laser beam.      T or F

- The potential location of injury to the eye is directly related to the wavelength of the laser radiation.  T or F

- Intrabeam viewing is allowed at CSULB.  T or F

- Most laser related eye injuries occur during beam alignments.  T or F

- Maximum permissible exposure (MPE) is defined as the maximum level of laser radiation which human tissue may be exposed to without harmful effect. T or F

- What two classes of laser potentially pose the highest level of hazard?

  - Class 1 & Class 2

  - Class 3 & Class 4

  - Class 5 & Class 6

  - All of the above

- If you intend to use a Class 3b or 4 laser at CSULB you are required to submit a Laser Use Authorization (LUA) to the Laser Safety Officer. T or F

- In general, it is better to control laser hazards through the use of engineering (i.e. beam stops, beam tubes) and administrative (i.e. written procedures) controls rather than rely solely on laser protective eyewear.  T or F

- The CSULB, laser safety program is based on the

        - Cal/OSHA regulations

        - American National Standard Z136.1

        - Food and Drug Administration

        - CDC/NIH guidelines

        - a. and b.

- All laser protective eyewear must be marked with the absorption wavelength and the optical density (OD) at that wavelength.  T or F

- Any kind of laser warning signs can be used at the entrances to a laser facility T or F

- All doors to rooms that contain a class 3b, or 4 lasers are to be posted with a sign marked “WARNING” and contain specific laser information.  T or F

- The “Retinal Hazard Region” refers to:

        - laser radiation in the 400 to 1400 nm range.

        - Location on the retina where light focuses

        - Laser radiation in the 180 to 315 nm range.

- A continuous wave (CW) laser with a beam power exceeding 0.5 Watt can ignite or cause off gassing from combustible materials that are in the beam path  T or F

- Standard operating procedures (SOPs) are required for which class of laser?

        - Class 3R

        - Class 3B

        - Class 4

        - b. and c.

        - All of the above

- For wavelengths that focus in the retina (400nm to 1400nm), the human eye has an optical gain up to.

        - 10X

        - 25X

        - 100,000X

        - 100X

- The most lethal non-beam hazard associated with high power lasers involves

        - Chemical exposure

        - Electrocution

        - Laser generated air contaminants

        - Cryogenic burns

- Unintended items in the beam path may result in a ______________ or _______________ reflection of the laser beam

        - Specular; diffuse

        - Contorted; curved

        - Blocked; attenuated

- Some of the ancillary hazards associated with the use of lasers include:

        - Chemical hazards

        - Cryogenic hazard

        - Smoke and fumes

        - High voltage

        - All of the above

- UV lasers and UV excitation systems may present a hazard to the ___________ as well as the eye.

- Whenever possible, you should enclose as much of the beam as possible without interfering with the application.  T or F

- The acronym MSDS stands for

        - Maintenance service docket sticker

        - Missing system data suppression

        - Material safety data sheet

        - macular semi-conductor duplex system

- Retinal eye damage occurs in which range of the electromagnetic spectrum?

  - Visible region 400 to 1400 nm

  - Near UV 315 to 390 nm

  - X-Ray below 100 nm

  - Mid UV 180 to 315 nm

- What are the two main characteristics to consider when choosing eyewear?

  - Style and fit

  - OD and wavelength

  - Price and frame

  - Plastic or glass

- You should never sit or stand at eye level to the laser table because

  - You might get sleepy

  - The ergonomics are bad

  - You are more likely to be struck in the eye by a stray beam

  - It’s OK to sit at eye level to the laser table

- What laser hazard is associated with the laser beam?

  - Electrical

  - Radiological

  - Chemical

  - Biological

- What is an example of an engineering control measure with respect to operating a laser?

  - An interlock circuit that turns laser off when door is open

  - Water-cooled lasers

  - Turning on a "Laser In Use" warning light outside of lab

  - Wearing laser safety glasses

Signature________________________  Date__________

Supervisor________________________

CSULB Laser Safety Quiz.doc